MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING AND URBAN DEVELOPMENT

STATE DEPARTMENT FOR TRANSPORT

AIR ACCIDENT INVESTIGATION DEPARTMENT

PRELIMINARY REPORT

OPERATOR/OWNER			:	Flight Training Centre Limited

AIRCRAFT TYPE/ MANUFACTURER	:	Cessna 152/Cessna Aircraft Company

YEAR OF MANUFACTURE		:	1978

AIRCRAFT REGISTRATION		:	5Y-CCQ

AIRCRAFT SERIAL NUMBER		:	15282790

DATE OF REGISTRATION		:	23 April 2013

NUMBER AND TYPE OF ENGINE	:	One Continental O-235-L2C

DATE OF OCCURRENCE		:	11 May 2018

TIME OF OCCURRENCE			:	1205 hours

LOCATION OF OCCURRENCE	:	Moi International Airport, Mombasa (HKMO)

(4.0355°S, 39.5973°E)

TYPE OF FLIGHT				:	Training

NUMBER OF PERSONS ON BOARD	:	One

INJURIES	:	None

NATURE OF DAMAGE	: 	Substantial damage to the NLG, propeller,

engine and lower fuselage section

CATEGORY OF OCCURRENCE	:	Serious Incident

PILOT IN COMMAND (PIC)		:	SPL

PIC’S FLYING EXPERIENCE		:	35 hours

Times given in this report are East African Local Time

REMARKS

On 11 May 2018 at 1300, the Air Accident Investigation Department was notified of a serious incident at Moi International Airport Mombasa by the Air Traffic Control Tower. The incident involved a Cessna 152 of registration 5Y-CCQ operated by Flight Training Centre Limited. During a touch-and-go landing on runway 21 of HKMO, the aircraft’s Nose Landing Gear (NLG) was broken resulting in a nose over of the aircraft and subsequent propeller strike on the runway surface.

On 11 May 2018 at 1152, 5Y-CCQ took off from runway 21 with a student pilot conducting solo circuits. The student was cleared to conduct right hand circuits after takeoff. The first circuit was reported to have been conducted successfully. Takeoff for the second circuit was reported to have been satisfactory. On final approach, the student reported to Tower that he was going for another touch-and-go. 5Y-CCQ was then cleared for a third circuit. The student reported that he experienced a strong crosswind on finals. In the process of correcting the aircraft for crosswind, the aircraft bounced twice on touchdown. On the third contact with the runway, 5Y-CCQ touched down with the nose wheel first. As a result, the NLG strut was broken. The aircraft then nosed over resulting in a prop strike. 5Y-CCQ slid on the runway as its front lower fuselage section made contact with the surface. The aircraft came to a complete stop just before intersection B of HKMO.

There were no injuries reported as a result of this occurrence. However, 5Y-CCQ sustained substantial damage that resulted in broken NLG strut, broken engine mounting, curled propeller blades and abrasion on the front lower fuselage skin.

The investigation is in progress.

Rufus Mutwol

Investigator-In-Charge

25/05/2018