MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING & URBAN DEVELOPMENT

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION DIVISION

PRELIMINARY REPORT

OPERATOR					:	PHOENIX AVIATION

AIRCRAFT TYPE/ MANUFACTURER	: 	AW119 MKII

YEAR OF MANUFACTURE		:	2016

AIRCRAFT REGISTRATION		:	5Y-RBY

AIRCRAFT SERIAL NUMBER		:	14918

DATE OF REGISTRATION			:	27/01/2017

NUMBER AND TYPE OF ENGINE		: 	One Pratt & Whitney Canada PT6B-37A

DATE OF OCCURRENCE			:	17 March 2018

TIME OF OCCURRENCE			:	0600

LOCATION OF OCCURRENCE: 	PLACE OF OCCURRENCE			:	Kitale

TYPE OF FLIGHT				:	Commercial

NUMBER OF PERSONS ON BOARD	:	2

INJURIES: 	INJURIES TO PERSONS ONBOARD	:	None

DNATURE OF DAMAGE: 	DAMAGE TO AIRCRAFT			:	Slight

CATEGORY OF OCCURRENCE:	CATEGORY OF ACCIDNET		:	Accident

PIC FLYING EXPERIENCE			:	2500 hours

Times given in this report are Coordinated Universal Time (UTC)

East African Local Time is UTC plus 3 hours.

REPORT

On 19th March 2018, the AAID received information about an aircraft accident involving AW119 type of helicopter registration 5Y-RBY operated by Phoenix Aviation Ltd while carrying a commercial flight at Kitale. According to the preliminary information, the helicopter departed Nairobi Wilson airport on 16th March 2018 at 1230 hours with six passengers onboard to Eldoret. The pilot had planned to land at Eldoret airstrip which is nearer Eldoret town instead of Eldoret International Airport which is 15km away from town. On arrival, the pilot landed at Eldoret International Airport at 1440 hours purposely to refuel the helicopter before proceeding to his final destination (Eldoret airstrip). After refueling the pilot successfully took off and landed at Eldoret airstrip where all the passengers disembarked the helicopter.

At 1600hours he took-off from Eldoret airstrip and landed at Kitale farm at 1615 hours for an overnight stay and rest with arrangement to wake up the following day and pick the passengers at Eldoret airstrip  back to Nairobi.

On the morning of 17th March 2018 at 0500hrs the pilot woke as usual and carried out Pre-flight inspection, checks and start. All the pre-flight checks and start all went well. The pilot took off from an open field with one passenger on-board, lifted up to 100ft above ground level before attempting transiting to forward flight. While executing forward transition at a distance of 50ft from point of departure, ‘’low rotor RPM’’ audial warning accompanied with master caution lights cockpit display & MFD Indication of rotor RPM decaying “ warning came on. As precautionary measure, the pilot elected for an emergency landing. He had not gained much altitude and so he decided to land the helicopter on an open farm immediately available nearby. So the pilot lowered the collective to try and recover the RPM, decelerated and managed to land the helicopter. On landing since the rotors had not fully recovered he experienced a hard landing on touch down but managed to switch off all power and fuel shut-off valve and evacuated the passenger.

DAMAGE TO AIRCRFAT

Post impact inspection observed that the main rotor blades had dropped and contacted the front wire cutter damaging it as well as breaking the upper section of the helicopter wind shield. The tail rotor drive shaft also broke at the middle as the tail rotor contacted the ground. Both tail rotor and the tail skid contacted the ground and bent.

Investigation is on-going to establish cause of the accident.

M. A. Ombasa

Investigator in charge

23/03/2018