MINISTRY OF TRANSPORT AND INFRASTRUCTURE

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION DIVISION

PRELIMINARY REPORT

OPERATOR:						Penial Air Ltd

AIRCRAFT TYPE/ MANUFACTURER: 		C208/ Cessna Aircraft Company

YEAR OF MANUFACTURE:			1992

AIRCRAFT REGISTRATION:			5Y-SAV

AIRCRAFT SERIAL NUMBER:			0312

DATE OF REGISTRATION:				29 July 2016

NUMBER AND TYPE OF ENGINE: 		One Pratt & Whitney PT6A-114

DATE OF OCCURRENCE:				11 April 2018

TIME OF OCCURRENCE:				1405

LOCATION OF OCCURRENCE: 	El Barde

TYPE OF FLIGHT: 					Commercial

NUMBER OF PERSONS ON BOARD: 		Fourteen

INJURIES: 	None

NATURE OF DAMAGE: 	Port horizontal stabilizer and elevator damage

CATEGORY OF OCCURRENCE:	Incident

PIC FLYING EXPERIENCE: 			Total Time: ~15,500 hrs (On Type: ~1,000 hrs)

Times given in this report are Coordinated Universal Time (UTC)

East African Local Time is UTC plus 3 hours.

REMARKS

At approximately 0800 on 12 April 2018, the Aircraft Accident Investigation Department (AAID) became aware of an occurrence in Somalia.

The pilot in command (PIC) had departed from Mogadishu earlier in the day on 11 April with fourteen persons on board and landed uneventfully at El Barde. He commenced his take off roll at about 1400 with the point of intended landing as Mogadishu with fourteen persons on board and 450 litres of fuel that translated to about four and half hours endurance. The PIC states that while on the take off roll, the horizontal stabilizer was apparently impacted by a stone. He proceeded to bring the aircraft to a stop, shut down the engine and disembark the passengers.

Based on his own assessment of the damage, he elected to fly the aircraft to what he considered the nearest safest place the next morning. He departed El Barde at 0325 on the 12 April and landed in Wajir airport at 0515. He states that upon landing, he inspected the aircraft and realized the damage had become more pronounced. He then contacted the Approved Maintenance Organisation (AMO) which was in charge of the aircrafts maintenance. The AMO advised that the aircraft not be flown further but remain at Wajir awaiting necessary maintenance actions to be performed.

Findings

Aircraft departed El Barde with known damage to the left horizontal stabilizer

AMO was not contacted for release to service prior to continued flight

AAID was not contacted to report the occurrence

Conclusion

It appears that a decision was made to fly an aircraft that was possibly not airworthy due to damages sustained prior. The  AAID shall not be investigating the incident further.

Recommendation

KCAA conduct a regulatory/compliance investigation into the occurrence

KCAA to ensure that the Operator, specifically the pilots in their employ are well aware of applicable laws, regulations and procedures regarding “no fly” items.

KCAA to audit the Operators safety management system particularly in regard to operations into and out of remote areas

Kithinji N.M.

Investigator-In-Charge

23/05/2018

ADDITIONAL PHOTOS