MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING AND URBAN DEVELOPMENT

STATE DEPARTMENT FOR TRANSPORT

AIR ACCIDENT INVESTIGATION DEPARTMENT

PRELIMINARY REPORT

OPERATOR/OWNER			:	Skyward Express Limited

AIRCRAFT TYPE/ MANUFACTURER	:	Fokker 27 MK 050/Fokker Services B.V.

YEAR OF MANUFACTURE		:	1990

AIRCRAFT REGISTRATION		:	5Y-SMQ

AIRCRAFT SERIAL NUMBER		:	20202

DATE OF REGISTRATION		:	06 September 2016

NUMBER AND TYPE OF ENGINES	:	2 × PWC PW125B

DATE OF OCCURRENCE		:	13 May 2018

TIME OF OCCURRENCE			:	1100 hours

LOCATION OF OCCURRENCE	:	Kisimayu Airport (HCMK)

PHASE OF FLIGHT			:	Pre-flight

TYPE OF FLIGHT				:	Ferry for maintenance

NUMBER OF PERSONS ON BOARD	:	Four

INJURIES	:	None

NATURE OF DAMAGE	: 	Minor

CATEGORY OF OCCURRENCE	:	Incident

PILOT IN COMMAND (PIC)		:	ATPL

PIC’S FLYING EXPERIENCE		:	10000 hours

PIC’S TOTAL HOURS ON TYPE	:	2000 hours

Times given in this report are East African Local Time

Figure 1: 5Y-SMQ

NARRATIVE

On 13 May 2018 at 1139, the Air Accident Investigation Department was notified of an imminent occurrence at Wilson Airport by the Air Traffic Control (ATC) Tower. A Fokker 27 MK 050 of registration 5Y-SMQ (SMQ) operated by Skyward Express Limited (Skyward) was en-route from Kisimayu Airport (HCMK), Somalia, to Nairobi Wilson (HKNW) when the Flight Crew (FC) contacted ATC indicating that they were experiencing landing gear (LG) problems.

According to the operator, SMQ operates locally in Somalia under a lease agreement with a local operator Ocean Airlines. On the morning of 13 May 2018, the crew were preparing SMQ for a scheduled flight from Kisimayu – Mogadishu – Garowe. During the preflight inspection, the mechanic noticed that one of the bolts on the left Main Landing Gear (MLG) yoke was loose and there was a crack on the locking plate of the bolt. After consultation with the company base in Nairobi, a decision was made to cancel the scheduled flight from Kisimayu to Mogadishu.

The FC reported that after assessment of the situation in consultation with the company base, a decision was made to ferry the aircraft to Nairobi Wilson to rectify the defect since there was no jacking equipment in Kisimayu. According to the FC, a decision was then made that it was safe to conduct the ferry flight to Nairobi for maintenance with the defect unresolved.

5Y-SMQ took off from HCMK at approximately 0930 for the ferry flight to HKNW with four persons on board – two pilots, a mechanic and a passenger. According to the FC, after takeoff the LG retracted and locked normally. However, while en-route and to avoid another cycle of gear extension, landing and retraction at Wajir with the defect unresolved, the FC made a special request to Area Control to fly directly to HKNW. The FC reported to Area Control that they had a LG problem and they were to fly directly to HKNW. During descend to HKNW, the FC alerted the ATC Tower that they were going to make a precautionary landing. When the duty air traffic controller asked if they needed any assistance, the FC replied in the negative.

SMQ landed safely on runway 07 at around 1151 and was taxied to the Skyward maintenance hangar without further event. The aircraft was inspected and the cracked locking plate replaced. The aircraft was released back to service after the inspection and replacement of the locking plate.

There were no injuries reported as a result of this occurrence. The damage was limited to the cracked locking plate of the left MLG yoke bolt.

Following this incident, the operator reported that they had introduced a new procedure to ensure that the yoke bolts are inspected before flight.

No further investigation of this incident was conducted.

Figure 2: Failed locking plate of the 5Y-SMQ left MLG yoke bolt

Rufus Mutwol

Investigator-In-Charge

26/05/2018