MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING, URBAN DEVELOPMENT AND PUBLIC WORKS

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION

PRELIMINARY REPORT

OPERATOR:					Bluebird Aviation Ltd

AIRCRAFT TYPE:					DASH 8 – 102A Series

AIRCRAFT MANUFACTURER: 			Bombardier Inc.

YEAR OF MANUFACTURE:			1 June 1993

AIRCRAFT REGISTRATION:			5Y-VVT

AIRCRAFT SERIAL NUMBER:			362

DATE OF REGISTRATION:			September 2008

TYPE OF ENGINE:				1x PW 120A

DATE OF OCCURRENCE:			31 October 2018

TIME OF OCCURRENCE:			1250

LOCATION OF OCCURRENCE:	Wilson Airport, Nairobi County

TYPE OF FLIGHT:					Test Flight

NUMBER OF PERSONS ON BOARD:		4

INJURIES:	Nil

NATURE OF DAMAGE:	Nil

CLASS OF OCCURRENCE:	Incident

PIC’S FLYING EXPERIENCE: 		9,500 Hours

PIC LICENSE	YK-6251 AL

All times given in this report are Coordinated Universal Time (UTC) East African Local Time is UTC plus 3 hours.

PHOTO

5Y-VVT after the incident

REMARKS

On the 31 October, 2018, Air Accident Investigation Department was notified of an occurrence at Wilson Airport in Nairobi County. The occurrence involved a Dash 8 – 102A series aircraft registration 5Y-VVT conducting a post test flight subject to a return to service check that had been carried out.

The pilot reported that the aircraft had taken off from Wilson Airport at 1228 for a test flight and landed back at 1250 when the incident took place.

In his statement the pilot indicated to have experienced unusual pull to the left during takeoff roll which demanded too much rudder input and tapping of the brakes to maintain directional control. The flight was uneventful until touch down and taxi phase when the pilot decided to demonstrate to the engineer who was onboard how the aircraft was behaving during takeoff. It was during this time that the pilot advanced power on the right engine making the aircraft drift sharply to the left, veering off the runway short of intersection of runway 07 and taxiway C. He immediately shut down the engines.

The aircraft came to a stop approximately 5 metres from the runway.

The aircraft sustained no damage and no injuries were reported. At the time of the incident the weather was CAVOK with calm winds.

Fredrick Kabunge

Investigator - In - Charge

31 October 2018