MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING AND URBAN DEVELOPMENT

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION DEPARTMENT

PRELIMINARY REPORT

OPERATOR					:	Etihad Airways

AIRCRAFT TYPE/ MANUFACTURER	: 	Airbus A320-232 / Airbus

YEAR OF MANUFACTURE		:	2014

AIRCRAFT REGISTRATION		:	A6-EIX

AIRCRAFT SERIAL NUMBER		:	6134

DATE OF REGISTRATION		:	24 June 2014

DATE OF OCCURRENCE			:	06 January 2018

TIME OF OCCURRENCE			:	1357 hours

LOCATION OF OCCURRENCE	:	Jomo Kenyatta International Airport (JKIA)

(Parking Bay 8 (S011943.82, E0365527.35))

DEPARTURE AERODROME	:	JKIA (HKJK)

DESTINATION AERODROME	:	Abu Dhabi Int’l Airport (AUH)

TYPE OF FLIGHT				:	Commercial Air Transport (Passenger)

FLIGHT №					:	EY642

NUMBER OF PERSONS ON BOARD	:	One hundred and forty one (141)

INJURIES	:	None

NATURE OF DAMAGE	: 	Crack and dent on the rear outboard right engine

cowling

CATEGORY OF OCCURRENCE	:	Ground Incident

GROUND HANDLING AGENT	:	Swiss port International Limited

PILOT IN COMMAND (PIC)		:	TBD

PIC FLYING EXPERIENCE		:	TBD

Times given in this report are East African Local Time

REMARKS

On the afternoon of 6 January 2018, the Air Accident Investigation Department was notified of a ground incident at JKIA by the Air Traffic Control (ATC) Tower. The incident involved an Airbus A320-232 of registration A6-EIX (EIX) operated by Etihad Airways. A conveyor belt loader operated by Swiss port International Limited collided with the aircraft starboard engine during pre-departure preparations.

EIX arrived from AUH on 6 January 2018 at 1308 and was scheduled to depart the same day at 1405 for AUH. Upon arrival, EIX was parked at Bay 8 of Apron 1, JKIA. A conveyor belt loader № SPCB 06 was then positioned at the aft cargo compartment № 3/4 to facilitate offloading of arriving baggage and cargo and the eventual loading for departure. At approximately 1350, loading of the aft cargo compartment was reported to have been almost complete awaiting loading of some extra baggage from the forward cargo compartment. At 1357, the conveyor belt loader № SPCB 06 reversed on its own, without an operator, from its stationary position at the aft cargo compartment, colliding with a baggage trolley which was located approximately 6 meters away from the aircraft, aft of the conveyor belt loader. After impacting the trolley, the direction of movement of the conveyor belt loader changed by about 180° and it then headed towards the right engine. The conveyor belt loader SPCB 06 impacted on the right engine resulting in a crack and dent on the rear outboard cowling.

Passenger boarding was reported to have been ongoing but almost complete at the time of occurrence. There was no injury reported as a result of the ground collision incident. Visible damage on the right engine was limited to the rear outboard cowling. The flight was cancelled after assessment of the damage.

The investigation is in progress.

CHIEF INVESTIGATOR OF ACCIDENTS

19/01/2018

________________________________________________________________