MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING AND URBAN DEVELOPMENT

STATE DEPARTMENT FOR TRANSPORT

AIR ACCIDENT INVESTIGATION DEPARTMENT

PRELIMINARY REPORT

OPERATOR/OWNER			:	Nairobi Flight Training Limited (NFT)

AIRCRAFT TYPE/ MANUFACTURER	:	Piper PA 28-140/Piper Aircraft Corporation

YEAR OF MANUFACTURE		:	1966

AIRCRAFT REGISTRATION		:	5Y-BON

AIRCRAFT SERIAL NUMBER		:	28-22452

DATE OF REGISTRATION		:	5 September 2017

NUMBER AND TYPE OF ENGINE	:	One Lycoming O-320-E3D

ENGINE SERIAL NUMBER		:	L-30675-27A

DATE OF OCCURRENCE		:	6 September 2018

TIME OF OCCURRENCE			:	1058 hours

LOCATION OF OCCURRENCE	:	Nairobi National Park

(01°20.446ʹS; 036°49.809ʹE)

TYPE OF FLIGHT				:	Training

NUMBER OF PERSONS ON BOARD	:	Two

INJURIES	:	None

NATURE OF DAMAGE	: 	Dents and scratches to the wing and horizontal

stabilizer skin and leading edges and spinner

CATEGORY OF OCCURRENCE	:	Serious Incident

PILOT IN COMMAND (PIC)		:	CPL

PIC’S FLYING EXPERIENCE		:	670 hours

Times given in this report are East African Local Time

REMARKS

On 06 September 2018 at 1112 hours, the Air Accident Investigation Department was notified of a serious incident at the Nairobi National Park by Wilson Airport Air Traffic Control Tower. The incident involved a Piper PA 28 of registration 5Y-BON operated by NFT. The aircraft was reported to have lost power after takeoff and made an emergency landing at the Nairobi National Park.

5Y-BON took off from runway 14 of Wilson Airport on 06 September 2018 at 1057 hours with two pilots on board. According to the PIC, the purpose of the flight was to build flight time on the PA 28. The flight was intended to take 30 minutes in the local training area and 15 minutes of circuits. Preflight checks and engine power runs were conducted prior to takeoff and according to PIC, everything was satisfactory. The aircraft accelerated slowly during the takeoff roll and the PIC reported initiating rotation at 80KIAS. Immediately after lift off, the engine started vibrating. According to the PIC, RPM at this point was below 2000 and airspeed had dropped below 80KIAS. The aircraft was approximately 600 feet above ground level. The PIC initially decided to request for a low-level flight back to Wilson, but the aircraft could not maintain a level flight. The stall warner light was reported blinking and the aircraft was losing altitude. The PIC then decided to make an emergency landing at the National Park. The airspeed and RPM were reported to have dropped to 60KIAS and 1800 respectively before touchdown. The aircraft rolled for approximately 100 meters before coming to rest.

Both pilots on board 5Y-BON at the time of incident were CPL holders. The PIC was a flight instructor at NFT while the second pilot was a Multi-Engine IR student also at NFT. The second pilot was reported to have been an observer and played no flying role during the incident flight.

There were no injuries reported as a result of this incident. The aircraft, however, sustained dent and scratch damage to the wing and horizontal stabilizer skin and leading edges and the spinner as a result of impact with shrubs during ground roll.

The investigation is in progress.

Rufus Mutwol

Investigator-In-Charge

20/09/2018