MINISTRY OF TRANSPORT, INFRASTRUCTURE, HOUSING & URBAN DEVELOPMENT

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION

PRELIMINARY REPORT

OPERATOR:						Kenya Wildlife Service

AIRCRAFT TYPE: 	                                     	Husky A-1B

MANUFACTURER:                                                  Aviat Aircraft Inc

YEAR OF MANUFACTURE:			1999

AIRCRAFT REGISTRATION:			5Y-KWG

AIRCRAFT SERIAL NUMBER:			2018

DATE OF REGISTRATION:				05 November 2010

NUMBER AND TYPE OF ENGINE: 		One Lycoming O-360-A1P

DATE OF OCCURRENCE:				17 June 2017

TIME OF OCCURRENCE:				0400

LOCATION OF OCCURRENCE: 	Lake Jipe airstrip, 3°37’16”S 37°46’52”E, Tsavo West National Park, Taita Taveta County

TYPE OF FLIGHT: 					Aerial patrol

NUMBER OF PERSONS ON BOARD: 		Two

INJURIES: 	None

NATURE OF DAMAGE: 	Minor

CATEGORY OF OCCURRENCE:	Incident

PIC:							YK-6878-PL

PIC FLYING EXPERIENCE: 			1,200 hours (600 hours on type)

Times given in this report are Coordinated Universal Time (UTC)

East African Local Time is UTC plus 3 hours.

REMARKS

At approximately 0600 on 17 June 2017, Air Accident Investigation Department (AAID) was notified of an occurrence at Lake Jipe airstrip, Tsavo West National Park, Taita Taveta County involving 5Y-KWG. The information received indicated that while on landing roll, the aircraft suffered gear collapse.

The aircraft had departed from Kamboyo airstrip, within Tsavo West National Park, at approximately 0300 with the pilot and one other occupant. The pilot stated that he had a full tank (52 gallons of which 50 gal. is useable fuel) of fuel which translates to approximately 5 to 6 hrs endurance. After approximately one hour of flight, the pilot elected to land at Lake Jipe airstrip, due to low cloud cover. His intention was to wait for the about 20 minutes on ground in the hope that the cloud cover would lift so that they could resume the aerial patrol (the aerial patrol they were conducting required them to observe the ground from the air therefore low clouds would compromise on visibility and therefore pose as a hindrance to the mission).

The aircraft touched down uneventfully however during the landing roll, the pilot reports that he heard a snapping sound and felt the propeller and one wing make contact with the ground. Its landing gear collapsed and the aircraft veered to the right of the runway centre line and came to rest with the right wing tip in contact with the ground. He immediately proceeded to conduct shutdown procedures.

The pilot and occupant exited the aircraft.

One blade of the two bladed propeller appeared slightly bent. The right wing upper surface appeared wrinkled near the tip.

Investigation will be handed over to the duty investigator.

Kithinji N.M.

19/06/2017

__________________________________________________________________