MINISTRY OF TRANSPORT, HOUSING AND URBAN DEVELOPMENT

STATE DEPARTMENT OF TRANSPORT

AIR ACCIDENT INVESTIGATION

PRELIMINARY REPORT

OPERATOR:						Ninety Nines Flying School

AIRCRAFT TYPE/ MANUFACTURER: 		Cessna 172/ Cessna Aircraft Company

YEAR OF MANUFACTURE:			1970

AIRCRAFT REGISTRATION:			5Y-NNG

AIRCRAFT SERIAL NUMBER:			172-59435

DATE OF REGISTRATION:				01/08/2012

NUMBER AND TYPE OF ENGINE: 		One Lycomming

DATE OF OCCURRENCE:				25/03/2017

TIME OF OCCURRENCE:				0630

LOCATION OF OCCURRENCE: 	Wilson Airport, Runway 07

TYPE OF FLIGHT: 					Training

NUMBER OF PERSONS ON BOARD: 		One

INJURIES: 	Nil

NATURE OF DAMAGE: 	Slight damage

CATEGORY OF OCCURRENCE:	Serious Incident

PIC FLYING EXPERIENCE: 			SPL

Times given in this report are Coordinated Universal Time (UTC)

East African Local Time is UTC plus 3 hours.

Picture: 5Y-NNG after the accident at Wilson Airport

REMARKS

On 25th March 2017 at around 0930 local time, a C172 aircraft registration 5Y-NNG owned and operated by Ninety Nines (99) Flying School; a certificated Aviation Training Organization (ATO) was involved in a runway excursion at Wilson Airport (WAP) runway 07.

At the time of the occurrence the weather at WAP was: wind 090/5, visibility over 10 km cloud base at 22000ft, temperature 16°c, dew point 16% and QNH 1022.5. The aircraft was operated by a student pilot (SP) on a solo flight who had accumulated 32.8 flight times. The Flight Instructor (FI) flew with the student on the first circuit to assess the student’s performance and then released the SP to continue with solo circuits.

The SP made three successful touch and go landings/approaches. On the fourth and final circuit the SP turned base overhead the military barracks. Upon aligning the aircraft for final approach he noticed another aircraft that was ahead and on the runway. (An instructor was on board the aircraft ahead of 5Y-NNG and was also training on touch and go maneuvers).  He continued the approach and noticed that his proximity to the other aircraft was drastically diminishing. By the time he was overhead threshold of runway 07, the other aircraft was still on the runway. The SP elected to to land on the grass area left of runway 07.

On touch down, the aircraft ballooned twice on the grass before coming to a complete stop at the edge of taxiway B intersection with the runway in a nose down attitude. The front landing gear was severed at the middle and the aircraft rolled on the ground for forty meters after colliding with the signage board. There was no post or pre-crash fire

The physical damage to the aircraft was on the front landing gear, left wing tip, propeller blades, spinner, and engine compartment underside. No injuries were reported on the sole occupant.

Further investigation is in progress

Chief Investigator of Accidents

31/03/2017

__________________________________________________________________________________